## Slide 1: A3 Project
Abhishek, Ankita, Rajat, Tang, Zhong

## Slide 2: Index
Business Context
Business constraints
Technical constraints
Quality attributes
High level functional requirements
Initial Architecture design
Q&A

## Slide 3: Assumptions
The MessageManage is deployed within the museum in a local network.

## Slide 4: Business Context
Environmental control: Hearing, ventilation, and air conditioning (HVAC)
Security: intrusion, motion, and fire.
Sensors, controllers, and monitors

## Slide 5: Business constraints
Sensors, controllers, and monitors can be easily added during runtime.
Messages are delivered reliably in a timely fashion.
Limited resources
Fixed schedule

## Slide 6: Technical constraints
Using Java, RMI.
Extending existing system
MessageManager cannot be modified.
Message format is already defined.
Using simulators for sensors.
Follow message-oriented architecture pattern.

## Slide 7: Quality Attributes
Extensibility
New elements can be added during runtime
Source | Developers
Stimulus | Add new elements (sensors, controllers, or monitors)
Environment | Runtime
Artifact | The system
Response | Allows to add the new elements and continue to operate
Response measure | The new element is operational after X second.

## Slide 8: Quality Attributes
Performance
Report to the user no more than 3 seconds after the sensor pushes data
Source | Sensors
Stimulus | Send data
Environment | Normal operation
Artifact | The monitor
Response | Reports to the user / reflects the changes
Response measure | Within 3 seconds

## Slide 9: Quality Attributes
Performance
The user command from monitor should be executed by controllers within 3 seconds
Source | Users
Stimulus | Issue a command using a monitor
Environment | Normal operation
Artifact | Controllers
Response | Execute the command
Response measure | Within 3 seconds

## Slide 10: Quality Attributes
Reliability
The system should notify the user of not receiving messages from a sensor after 3 cycles of that sensor.
Source | Monitor
Stimulus | Not receiving messages from a sensor after 3 cycles
Environment | Normal operation
Artifact | Monitor
Response | Notify user and continue to collect messages
Response measure | NA

## Slide 11: Quality Attributes
Reliability
The monitor should notify the user if it doesn’t receive an acknowledgement from the controller after the monitor sends a message to the controller.
Source | Monitor
Stimulus | Not receiving acknowledgement from a controller
Environment | Normal operation
Artifact | Monitor
Response | Notify user
Response measure | After 2 seconds

## Slide 12: Quality Attributes
Security
The system should prevent unauthorized elements from connecting to the system
Cannot be achieved due to technical constraint

## Slide 13: Quality Attributes
Security
The system should ignore unrecognized messages and notify the users within the consoles (not creating new “security console”).

## Slide 14: High level functional requirements
System A
  Intrusion detection and monitoring
  3 alarms: window break, door break, and motion detection.
  Arm and disarm the system
  Simulate security alerts

## Slide 15: High level functional requirements
System B
  Fire detection and monitoring
  One fire alarm controller and one sprinkler controller
  Display fire alarm
  Confirm or cancel sprinkler action
  Confirm automatically after 10s without response.
  Turn off the sprinkler

## Slide 16: High level functional requirements
System C
  Service maintenance console
  List all elements and description
  Detect a device not responding and notify the user

## Slide 17: Initial Architecture design

## Slide 18: Initial Architecture design

## Slide 19: Initial Architecture design

## Slide 20
QA